## Slide 1: Microsoft RemoteFX GPU Virtualization Technology Deep Dive
Karthik Lakshminarayanan
Group Program Manager
Microsoft
VIR313

## Slide 2: Objectives and Agenda
Objectives
What is RemoteFX – Value proposition
How it works – Architecture
Agenda
RemoteFX and the space
  Background and Demo
Architecture on server and client
  Technology deep dive for VDI and RDSH
  USB Redirection with RemoteFX for VDI
  RDP 7.1 client side architecture
  RemoteFX Thin clients
2
Notes: Today’s talk will cover the value proposition and will have a demo. Then we will do a deep dive on the architecture and how each component works to deliver this great end user experience.

## Slide 3
RemoteFX Clients
Traditional PC
Requires a local IT Pro.
Consumes ~170W.
Cannot meet certain regulatory reqs.
Vulnerable to hardware failures.
Limited to PC form factors.
Windows Server & RemoteFX
Windows Server & RemoteFX
Manageable from anywhere.
Power footprint is shared.
Helps meet regulatory reqs.
Recoverable from hardware failures.
Enables full range of client form factors.
Aero Glass
Adobe Flash
Microsoft Silverlight
DirectX Apps
Windows Media
HTML 5
Traditional PC
Powerful
Flexible
Diverse
Versatile
Portable
3
Notes: When you talk about the desktop, you have to begin with the traditional PC. The PC has many advantages – it is a powerful device that runs a wide variety of applications, and is flexible - for offline and mobile scenarios, the PC is tough to beat. But it also has some drawbacks. For example, it requires a fair amount of power, it needs a local IT Pro to troubleshoot and maintain it. And if you have strict regulatory or compliance requirements, could be lot harder to implement. So traditionally, we have moved the desktops to the datacenter and ran it on a server. This has many advantages – until recently, most of these advantages were largely for the IT Pro. The user experience is average. As Windows 7 adoption grows and new web technologies like HTML5 evolve, providing a rich user experience will become a requirement. Modern browsers like IE9, FF4 and Chrome provide GPU acceleration – so GPUs are being used for web applications as well.
We want to enable a wider spectrum of thin client and zero client devices, so that managing these end point devices does not become a problem for the IT Pro. With RemoteFX, we can enable the full spectrum of client devices including a deployment that is just a keyboard, mouse, monitor and network.
With RemoteFX, VDI can be a win-win for the IT Pro AND the end user. Let’s look at a demo.

## Slide 4: Demo – RemoteFX In Action
VDI user
IT Pro Admin
4
Notes: Key talking points: full desktop experience, all delivered to a wide range of client devices including hardware based clients. You can deploy RemoteFX with entirely commodity hardware. Pass the 2 client devices around.
Media Center – Chess, Interactivity
Silverlight puzzle
Flip 3D
IE9 – Canvas demo
Demo – Device manager – do at the end

## Slide 5: Agenda
RemoteFX and the space
  Value Proposition and Demo
Architecture on server and client
  Technology deep dive for VDI and RDSH
  USB Redirection with RemoteFX for VDI
  RDP 7.1 client side architecture
  RemoteFX Thin clients
5

## Slide 6: New Concept for RDP 7.1
Separate host intercept for each graphics stack & client equivalents – gaps
Can lead to better bandwidth utilization for intercepted graphics types
RDP Client Rendering
RDP Host Rendering
Leverages Rich Client HW and SW
Single intercept point for all graphics – predictable and complete UX
Typically requires more bandwidth as traffic is sent as compressed bitmaps
Lightweight Clients & Complexity Shifted to Host
6
Notes: RDP 7.1 is the version that supports RemoteFX. We have changed the paradigm for RemoteFX, moving away from a client rendering model to a host rendering model. Specifically, client rendering is when the native content is intercepted and transmitted to the RDP client for rendering. In the host rendering model, all the content is rendered on the server and transmitted as bitmaps. So let us see how these compare:

## Slide 7: RemoteFX VDI Architecture Concepts
Enabling Technology
Customer Value
Intelligent screen capture and hardware-based encode
Host side rendering
vGPU
Full rich Windows experience
Remoting any content
Full range of client devices
Content and GPU independent intercept & rendering
Single GPU for multiple Hyper-V guests
High fidelity user experience
CODEC designed for text and image content
Single CODEC for VDI, RDS and WMS sessions
HW and software manifestations interoperable by design
Screen deltas sent to client based on network and client availability
Applications run at full-speed on host
Differentiating Innovation
Supports all USB devices.
Redirection over RDP.
No client side drivers needed.
Bitmap remoting and hardware-based decode
USB Device Redirection
Full range of
USB devices
Notes: USB redirection
  Allows you to redirect virtually any USB device transparently over RDP
Redirects devices at the USB Request Block (URB) Level
No client drivers necessary
One method that works with many devices
Only one session can use a USB device at a time
Optimized for the LAN
The Virtualized Graphics device technology enables the knowledge worker to run all graphical (2D and 3D) applications in a virtual machine, and it allows the IT admin to share a physical graphics device(s) across multiple knowledge workers in a graphics device agnostic fashion. The same VGPU driver will work irrespective of whether the underlying hardware is from NVIDIA, ATI, or any other vendor.
Remote any content – Host side rendering
Existing RDP technologies are based on primitive remoting and client side rendering. With the Calista release, the RDP Server will now support server side rendering, where the entire desktop screen is composed on the server. Applications will use the VGPU like any other graphics device, just like they do on a local PC. With this approach, the system no longer has to be updated for the next popular graphics format in the industry.
High fidelity UX – Intelligent screen capture and hardware based encode.
The primary goal for Calista is to deliver the local desktop like experience from the server to any client. Once the desktop screen is rendered on the host, the Calista system has effectively flattened the desktop content to a 2D bitmap. The system has an intelligent capture mechanism which can detect what changes between successive rendered bitmaps and pick and choose content based on the network condition. These changes are then compressed using the processing power of the GPU and the CPU.
The system also has an hardware implementation of the codec. This allows the VDI server to deliver a constant screen frame rate independent of the user workload, increases the user density per server, when compared to the software approach..
Any range of client devices – Bitmap remoting and hardware based decode
This standardization of the content to a bitmap enables any basic display client to consume this content. As long as a client display device has a basic 2D display engine, it will be able to render this 2D bitmap. There is no need of sophisticated graphics stack on the client. This piece of technology is absolutely game changing, as it enables the customer to get his full rich Windows experience not just on PCs but on any device with a display. We are working with hardware partners to integrate the codec chip into their devices, like LCD TVs, monitors, phones, handhelds, etc.

## Slide 8: Hyper-V VDI + RemoteFX Components
W7 SP1 Guest OS
VGPU Driver
Hyper-V Parent Partition
RCC
VMBUS
Hyper-V
Integrated Shared Memory
Comms
RDP
GPU
VGPU output rendered to physical GPU via DirectX.
Screen deltas captured from GPU.
First phase of CODEC runs on GPU.
Inter-VM Communications
Optionally offloads CODEC from CPU/GPU increasing fidelity and scale.
Protocol Fundamentals (e.g. Authn, Encryption)
vGPU (WDDM) driver exposes parent GPU to guest OS.
RemoteFX Hardware ASIC and Driver
WS08 R2 SP1 Hyper-V Server
8
Notes: Lets look at how these components are integrated with Hyper-V and the server

## Slide 9: RemoteFX-for-RDVH (VDI) Virtual GPU and Rendering Pipeline
IE9
Windows
App
RemoteFX Hyper-V VM Bus Parent Integration
RCC
Hyper-V VMBUS
Shared Memory
Comms
DX9 APIs
RemoteFX Hyper-V VM Bus Child Integration
RemoteFX VGPU Driver
DX9 APIs
GDI
GPU Vendor Driver
GPU
W7 Child Partition
Hyper-V Parent Partition
9

## Slide 10: RemoteFX-for-RDVH (VDI) Capture and Encoding Pipeline
RemoteFX Hyper-V VM Bus Parent Integration
RCC
RemoteFX Hyper-V VM Bus Child Integration
DX10 APIs
GPU Vendor Driver
GPU
Hyper-V Parent Partition
W7 Child Partition
RemoteFX ASIC DRIVER
RemoteFX ASIC
Hyper-V VMBUS
Shared Memory
Comms
User Mode RDP
RemoteFX VGPU Driver
RDP
10

## Slide 11: RemoteFX-for-RDSH (formerly TS)
User
Kernel
Session [1…n]
TS Core
LSM
TERMSRV
Session 0
RDPWSX
RDP Core
TERMDD
RDPWD
TDTCP
GDI
WIN32K.SYS
RDPDD (RDP Display Driver)
RemoteFX Encode Library
RemoteFX HW Encode Driver
RemoteFX Encode ASIC
CPU
Windows Server with RDSH Enabled
IE
Office
Other
RDP
Notes: RDPWSX – DLL that contains user mode extensions for server
RDPWD – RDP Winstation Driver - (the driver that does all the RDP VC Multiplexing, connection sequence and protocol framing).
TDTCP – TCP Pipe – Transport Driver

## Slide 12: RemoteFX for RDVH and RDSH – Cheat Sheet
 | RemoteFX for RDVH (VDI) | RemoteFX for RDSH (TS)
Hardware/Software Requirements |  | 
CPU with SLAT (SSE2 is a subset of SLAT) | X | 
CPU with SSE 2 | X | X
GPU installed in Host Server | X | 
Windows 7 SP1 virtual machine | X | NA
RDC 7.1 Client | X | X
Features/Benefits |  | 
GPU Virtualization | X | 
USB Redirection | X | 
Aero | X | 
RemoteFX Compression using software (CPU only for RDSH, CPU and GPU for VDI) | X | X
Offload RemoteFX CODEC to Hardware (Identical HW for TS and VDI) | X | X
12
Notes: SSE2 = Streaming SIMD Extensions 2

## Slide 13: The RemoteFX ‘Payload’
RemoteFX-enabled RDS Server Infrastructure
RemoteFX-enabled Remote Client
Remote Client
RDS Server Infrastructure
Remote Desktop Protocol (RDP)
RemoteFX
Graphics Virtual Channels (VCs)
Mouse & Keyboard VCs
Partner Virtual Channel Plug-Ins
Bulk Compression (RDP5+, RDP6.0, RDP6.1)
Virtual Channel Multiplexing and Framing
Security Layer (SSL/Kerberos/NTLM)
Transport Layer (e.g. TCP, RPC/HTTP, Windows Live Tunnel)
Device
VCs
RemoteFX leverages the RDP protocol structure
RDSH (TS)
RDVH
13

## Slide 14: RDP 7.1 Client Components and Graphics Pipeline
Core Services
Networking/
Security
Virtual Channels
Devices
Bulk Decompress
Key/Mouse
RemoteFX Decode Abstraction Layer
RDP 7 Graphics Providers (AERO, Windows Media)
RemoteFX SW Decoder
RemoteFX HW Decode Driver
RemoteFX Decode ASIC
CPU
Display Device
GPU
RDP Client Components
RDP
14

## Slide 15: RemoteFX USB Device Redirection for VDI
Versatile
  Rich and thin clients (no client drivers necessary)
  Use with any RemoteFX-enabled VM
  Admins control what devices can and cannot be redirected
Compatible
  Works with just about any USB device
  Applications are transparent to redirected devices
  Integrate with PnP/Windows Update for device installs
15

## Slide 16: Local USB Device Arrival (without RemoteFX)
Windows Kernel
(I/O Mgr, PnP)
USB HUB
2
Provided by:
Microsoft
IHV/ISV
USB Device
Driver
1
Application
3
4
User
Kernel
Win32 I/O API
Notes: Make this slide before Device Claim

## Slide 17: USB Redirection – RDP Client Side Behavior
USB Device
Driver
RDP Client
RemoteFX USB Hub Filter
USB HUB
2
3
Provided by:
Microsoft
IHV/ISV
RemoteFX VM on
RDVH Server
Remote FX Generic USB Driver
4
User
Kernel
1
RDP
5

## Slide 18: USB Redirection – VM Behavior
Windows Kernel
(I/O Mgr, PnP)
RemoteFX Device Proxy
RemoteFX USB HUB
6
USB Device
Driver
8
Provided by:
Microsoft
IHV/ISV
Application
Win32 I/O
API
9
RemoteFX VM on
RDVH Server
10
User
Kernel
7
Notes: Auto connect: we will not return a device to the client until all attempts will be completed
On the disconnect all redirected devices will be removed

## Slide 19: RemoteFX Ultra Lightweight Thin Clients
New class of Thin Client using ARM based designs
Works with Hyper-V VDI, RDSH and Multipoint Server
Running Windows CE, Linux, or in-house OS
Lower client resources
  CPU: 200 – 400 MHz
  Memory: < 256MB RAM, < 128MB Flash Memory
  Less than 5w power
Dedicated CODEC for acceleration
19

## Slide 20: RemoteFX Sizing Guide for VDI
Based on the display resolution and workload per VM, the following number of virtual machines could be loaded on a GPU
Can load additional non-RemoteFX VMs on the same server [e.g. HP RA has 65 non-RemoteFX VMs and 12 RemoteFX VMs on a 8 core server with a single 1.5 GB GPU]
* These are theoretical numbers of how many RemoteFX-enabled virtual desktops could fit on a GPU with given amount of video memory. They do not take into account the amount of GPU resources consumed by each virtual machine. The GPU resource consumption will vary from workload to workload. Actual numbers will vary based on the workloads executing in the virtual machines.
 | Maximum RemoteFX-enabled virtual desktops per GPU * |  |  | 
Resolution | 1 GB Nvidia FX3800 ATI V5800 | 1.5 GB Nvidia FX4800 | 2 GB ATI V7800 ATI V8800 | 4 GB Nvidia Quadro FX5800
1024x768 | 13 | 20 | 27 | 54
1280x1024 | 8 | 12 | 16 | 32
1600x1200 | 5 | 8 | 11 | 22
1920x1200 | 4 | 6 | 9 | 18
20

## Slide 21: In Closing
Call to Action | 
Watch for latest news | Watch the RDS blog for latest: http://blogs.msdn.com/b/rds/ Keep up to date on latest partner offerings by visiting http://www.microsoft.com/remotefx Download the Step by Step and Conceptual documents.
Evaluate | Evaluate fit for your users and environment. Download RTM of SP1 and exercise your scenarios.
Share and give Feedback | Share and ask through the Web Forum: http://forums.technet.microsoft.com/en/winserverTS/threads/
Questions and Answer
21

## Slide 22: Common Misconceptions About RemoteFX
The CAPEX of RemoteFX is higher because of GPUs.
The user density per server is lowered with RemoteFX.
RemoteFX scales to just a couple of VMs per GPU.
There are no RemoteFX ready servers in the market today from major server OEMs.
MS views RDSH as being of lower importance than VDI.
RemoteFX is for Aero only.

## Slide 23: Track Resources
Don’t forget to visit the Cloud Power area within the TLC (Blue Section) to see product demos and speak with experts about the Server & Cloud Platform solutions that help drive your business forward.
You can also find the latest information about our products at the following links:
Windows Azure - http://www.microsoft.com/windowsazure/
Microsoft System Center - http://www.microsoft.com/systemcenter/
Microsoft Forefront - http://www.microsoft.com/forefront/
Windows Server - http://www.microsoft.com/windowsserver/
Cloud Power - http://www.microsoft.com/cloud/
Private Cloud - http://www.microsoft.com/privatecloud/

## Slide 24: Resources
www.microsoft.com/teched
  Sessions On-Demand & Community
  Microsoft Certification & Training Resources
  Resources for IT Professionals
  Resources for Developers
www.microsoft.com/learning
http://microsoft.com/technet
http://microsoft.com/msdn
Learning
http://northamerica.msteched.com
  Connect. Share. Discuss.

## Slide 25
Complete an evaluation on CommNet and enter to win!

## Slide 26
Notes: New for TechEd 2011, we will be working with Microsoft Tag (http://tag.microsoft.com/overview.aspx) to create unique Tags for every session at the event. Your session Tag will appear on both the room signage and at the end of your presentation. With your session Tag, attendees will be able to scan as they enter the room to retrieve session details, view speaker bios, and engage in discussions; or scan at the end of the presentation to evaluate your session and download materials. We’re excited to integrate Microsoft Tag across the My TechEd mobile experience this year.

## Slide 27
© 2011 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.

## Slide 28: Industry Trends Leveraged By RemoteFX VDI
Infrastructure
  VM isolation enables full desktop centralization
  Processor evolution shifts from clock speed to massive parallelism
  Faster networks
  Increased diversity of client devices
Graphics related trends
  Graphics Richness Increasing: HTML5, Media, 3D UI, Video, Animations, Flash, Silverlight
  Increasing Fragmentation of Graphics Stacks
  Portable Graphics stacks like Silverlight and Flash Emit as Flattened Bitmaps
  Modern Browsers Leveraging GPUs where Available
28

## Slide 29: Backup

## Slide 30: RemoteFX OS & System Requirements for VDI
Hyper- V Host for VDI or RDSH
  Windows Server 2008 R2 with SP1
  (Hyper-V, Standard, Enterprise, and DataCenter editions)
VDI Virtual Machine
  Windows 7 Enterprise with SP1
  Windows 7 Ultimate with SP1
Remote Client Device [works with VDI, RDSH or Multipoint Server]
  Windows 7 with SP1
  Devices with RDP 7.1
30

## Slide 31: RemoteFX Requirements for RDSH
Requires Windows Server 2008 R2 Service Pack 1.
To use RemoteFX on an RD Session Host server, the processor on the RD Session Host server must support Streaming SIMD Extensions 2 (SSE2).
The RDSH role with RemoteFX can run as a virtualized workload on any hypervisor, since there is no dependency on a GPU.
Off by default. Enabled via a Group Policy
Recommended if your users will ever run any Flash, Silverlight or HTML5 content
31